## Slide 1
Mohamed Abuella, Student Member, IEEE, Badrul Chowdhury, Senior Member, IEEE
Department of Electrical and Computer Engineering
Energy Production & Infrastructure Centre (EPIC)
University of North Carolina at Charlotte, Charlotte, NC 28223-0001
Poster Qualifying Combined Solar Power Forecasts in Ramp Events' Perspective
1. Objectives
6. Conclusion
Applying a qualifying metric for solar power forecasts to assess their capability to predict the ramp events, especially by the combined forecasts, then those forecasts can be implemented for:
Managing high ramp-rates of PV solar power generation;
Optimal energy management of energy storage systems;
Voltage regulator settings on feeders with PV distributed generation.
5. Case Study
These are the most common metrics that are also used for our case study, the root mean square error (RMSE), mean bias error (MBE), and Skill Score (ss) as common metrics are chosen to evaluate the forecasts. In addition, a proposed metric which depends on ramp rates of solar power is explained below:
4. Most Common Evaluation Metrics
The solar PV power system is located in Australia. The weather forecasts data and the measured solar power data were recorded from April 2012 to May 2014. The weather forecasts from European Center for Medium-Range Weather Forecasts (ECMWF), which is a global numerical weather prediction (NWP) model.
The test part of the data contains 12 months - from May 2013 to June 2014.
2. Definition of Solar Power Ramp Rates
Acknowledgement
The authors would like to acknowledge the support of Energy Production and Infrastructure Centre (EPIC) at UNC Charlotte.
To evaluate the ramp events of the forecasts, the ramp rate of each hour is calculated as in (1), and the RMSERR of the ramp rates is calculated below:
Fig. 5: The Combined forecasts improvement over the different models
where P(t) is the solar power of the target hour, it can also be its forecast F(t); D is the time duration for which the ramp rate is determined.
Fig. 1: (a) Solar power forecasts and (b) their ramp rates for 2 days
Fig.4: (a) 24-hours-ahead forecasting and (b) combining methodology schemes of the hour-ahead forecasts on May 31st day
3. Evaluation Metrics
Table I
Evolution Metrics of Renewable Energy Forecasting
5.1. Data Description
This study qualifies the solar power combined forecasts in terms of solar power ramp events. Several forecasting models of solar power are implemented to generate various forecasts, and then those forecasts are combined by ensemble learning method, random forests (RF).
5.3. Results and Evaluation
Table II
RMSE of Different Models and Combined Forecasts
The evaluation metrics of solar power forecasting should be chosen based on the application of the forecasts.
However, the common evaluation metrics for the combined forecasts indicate that the combined forecast has the best performance. Although the combined forecasts are better than the individual forecasts, it does not necessarily mean that they are also the best for capturing the ramp events, this can be identified by using the proposed metric, the root mean square error of ramp rates (RMSERR).
In terms of ramp event forecasting, the combined forecasts are not the most efficient option for applications that rely on highly accurate ramp event forecasts.
In addition, the RMSERR reveals room for improvement of the ramp event forecasting using the combined forecast, which may be considered as further work of this study.
Fig. 2: Evaluation metrics in Renewable Energy Forecasting [Ref.1]
RMSE = Root Mean Square Error
MAE = Mean Absolute Error
MBE = Mean Bias Error
MAPE = Mean Absolute Percentage Error
SS = Skill Score
MSE = Mean Square Error
STD = Standard Deviation
R2 = Coefficient of Determination
MPE = Mean Percentage Error
CC = Correlation Coefficient
ME = Mean Error
MaxAE = Maxium Absolute Error
MeAPE = Median of the Absolute Percentage Error
MASE = Mean Absolute Scaled Error
where F is the solar power forecast and P is the observed value of the solar power. F and P are normalized to the nominal installed capacity of the solar power system, n is the number of hours, which can be day-hours or month-hours.
The improvement or the skill score (SS) metric is to compare a method with respect to other benchmark methods
where RRP and RRF are ramp rates of the observed solar power and the forecasts respectively
(6)
(5)
(3)
(2)
(4)
(1)
5.2. The Methodology
(7)
The first stage is to produce the 24-hour-ahead forecasts from the NWP data and the observed solar power, as shown in Fig. 4.a. The second stage, shown in Fig. 4.b is where the ensemble learning (i.e., the random forest) combines the available weather data and the previous forecasts from the first stage, all blended together to with the persistence model (i.e. an hour lagged solar power observations) for achieving better hour-ahead forecasts rather than day-ahead forecasts.
Table III
MBE of Different Models and Combined Forecasts
Chart: Improvement of Combined Forecasts over Other Models
| June | July | August | September | October | November | December | January | February | March | April | May
Persistence 48% | 0.45352 | 0.31053 | 0.44873 | 0.46607 | 0.53968 | 0.51941 | 0.57198 | 0.59306 | 0.45399 | 0.37654 | 0.46825 | 0.56868
MLR 18% | 0.16629 | 0.11469 | 0.16665 | 0.060634 | 0.18529 | 0.23244 | 0.19054 | 0.33297 | 0.28157 | 0.10379 | 0.19157 | 0.10125
ANN 8% | 0.087002 | 0.051609 | 0.11259 | 0.042686 | 0.12119 | 0.084701 | 0.076843 | 0.10598 | 0.10796 | 0.048719 | 0.049945 | 0.058918
SVR 12% | 0.10143 | 0.10725 | 0.13308 | 0.040256 | 0.15556 | 0.089606 | 0.12595 | 0.1659 | 0.22739 | 0.10958 | 0.12176 | 0.066088
Simple Avgerage 6% | 0.0016077 | -0.013597 | 0.050132 | 0.050685 | 0.096626 | 0.084211 | 0.10072 | 0.10476 | 0.062687 | 0.025445 | 0.057632 | 0.12755
Table III
RMSE and RMSERR of Different Forecasts over the Entire Year
To evaluate the ramp events capability of the combined forecasts, we implemented the evolution metric RMSERR as in (6):
Therefore, it is obvious that in terms of ramp events, the combined forecasts are not the best, although in terms of RMSE the combined forecasts are found the most accurate.
SVR
Persistence
Ensemble Learning (RF) for Combining the Models
Combined Forecasts
Individual Forecasting Models
MLR
ANN
Fig. 3: Diagram of combining the different forecasts
(8)
Since is the output of the random forest (RF)
Day-ahead forecasts
Hour | Day | Month
00:00-23:00 : 00:00-23:00 | 1 : 30 | June
00:00-23:00 : 00:00-23:00 | 1 : 31 | July
: : | : : | : :
00:00-23:00 : 00:00-23:00 | 1 : 30 | May
00:00 AM 01:00 AM : 23:00 PM | 31 | May
(a)
(b)
Training Set
(364 days)
at 00:00 AM
PV Power
Past solar power observations
Forecasts (model’s outcomes)
Weather Data
Past weather forecasts, including: solar irradiance, cloud cover, temperature, wind speed, humidity, precipitation, etc.
Future weather forecasts
Weather Data
Past weather forecasts, including: solar irradiance, cloud cover, temperature, wind speed, humidity, precipitation, etc.
Future weather forecasts
Models’ Outcomes
Past models’ outcomes, including: Day-ahead: MLR, ANN, SVR Hour-ahead: Persistence
Future models’ outcomes
PV Power
Past solar power observations
Hourly combined forecasts
[Ref.1] R. Ulbricht, A. Thoß, H. Donker, G. Grafe, and W. Lehner, “Dealing with Uncertainty: An Empirical Study on the Relevance of Renewable Energy Forecasting Methods,” in In Data Analysis for Renewable Energy Integration, Springer, 2016