## Slide 1
Wind and Solar Energy Modeling and Analysis
Technical Presentation
By
Mohamed Abuella
The University of North Carolina at Charlotte
August 6th, 2019

## Slide 2
Mohamed Abuella
An electrical engineer by training, traditionally is interested in Mathematical and Computational Analysis, Modeling and Optimization, and who is recently get passionate in Artificial Intelligence and Data-driven Analytics for Energy and Smart Grid applications.
Hobbies and Interests
Making Mediterranean Food and Drink, but also try my own out-of-box recipes;
Stretching, Walking, Running, or Swimming, Diving.. and hopefully Climbing; Wondering around and Discovering New Places, ..kind of adventure;
Watching, Reading and Sharing Stuff on Internet, useful & dumb things;
And more often just.. Chilling and Enjoy Doing Nothing!
Who am I ?

## Slide 3
Four U.S. Locations for Comparison of Renewable Energy Modeling and Analysis
Charlotte NC, Boston MA, Boulder CO, Tucson AZ.
Modeling for Different Locations in the U.S.
Data are retrieved from NREL’s Developer Network: https://developer.nrel.gov/
Wind and Solar Energy Modeling

## Slide 4
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Time series of wind speed at height 100m (m/s)
Wind Energy Modeling

## Slide 5
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Boxplots of monthly distribution of wind speed
Wind Energy Modeling

## Slide 6
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Wind Roses of Wind Speed
Distribution of wind direction and speed
Wind Energy Modeling

## Slide 7
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Probability density distribution of wind speed
Wind Energy Modeling

## Slide 8
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Wind turbine GE 1.5SLE 77m is utilized for modeling
The wind power curve for GE 1.5SLE 77m
to covert the wind speed to wind power
http://www.wind-power-program.com/Downloads/Databasepowercurves(May2017).zip
Wind Energy Modeling

## Slide 9
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Probability density distribution of wind power
Considering other parameters such as air pressure, temperature and density at the given height=100m
Wind Energy Modeling

## Slide 10
Charlotte, NC
Boston, MA
Boulder, CO
Tucson, AZ
Month0 | MWh | NCF
1 | 467.945 | 41.90%
2 | 584.361 | 58.00%
3 | 510.499 | 45.70%
4 | 512.191 | 47.40%
5 | 420.662 | 37.70%
6 | 239.808 | 22.20%
7 | 354.663 | 31.80%
8 | 285.923 | 25.60%
9 | 396.328 | 36.70%
10 | 504.488 | 45.20%
11 | 471.683 | 43.70%
12 | 691.553 | 62.00%
Month | MWh | NCF
1 | 387.574 | 34.70%
2 | 455.725 | 45.20%
3 | 410.236 | 36.80%
4 | 456.256 | 42.20%
5 | 381.352 | 34.20%
6 | 193.475 | 17.90%
7 | 230.690 | 20.70%
8 | 141.379 | 12.70%
9 | 197.738 | 18.30%
10 | 310.630 | 27.80%
11 | 355.663 | 32.90%
12 | 298.279 | 26.70%
Month | MWh | NCF
1 | 413.396 | 37.00%
2 | 288.217 | 28.60%
3 | 382.094 | 34.20%
4 | 339.568 | 31.40%
5 | 222.077 | 19.90%
6 | 187.928 | 17.40%
7 | 216.100 | 19.40%
8 | 215.737 | 19.30%
9 | 268.648 | 24.90%
10 | 206.966 | 18.50%
11 | 224.898 | 20.80%
12 | 312.770 | 28.00%
Month0 | MWh | NCF
1 | 262.764 | 23.50%
2 | 247.664 | 24.60%
3 | 259.804 | 23.30%
4 | 378.228 | 35.00%
5 | 184.679 | 16.50%
6 | 188.630 | 17.50%
7 | 111.523 | 10.00%
8 | 143.448 | 12.90%
9 | 223.078 | 20.70%
10 | 258.261 | 23.10%
11 | 236.885 | 21.90%
12 | 274.958 | 24.60%
Wind Energy Modeling
in 2009
Calculating the net capacity factor (NCF)
for each month, then over the entire year
NCF=
NCF=
Wind Energy Modeling

## Slide 11
Wind Energy Modeling
in 2009 and 2010
2009 | MWh | NCF
Charlotte | 3818.9 | 29.1%
Boulder | 3278.4 | 24.9%
Boston | 5440.1 | 41.4%
Tucson | 2769.9 | 21.1%
2010 | MWh | NCF
Charlotte | 3544.6 | 27.0%
Boulder | 2676.9 | 20.4%
Boston | 6107.7 | 46.5%
Tucson | 2969.9 | 22.6%
Chart: Yearly Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
2009 | 0.23144 | 0.25507 | 0.23448 | 0.24269
2010 | 0.27 | 0.204 | 0.465 | 0.226
Chart: Yearly Yeild of Wind Energy
| Charlotte | Boulder | Boston | Tucson
2009 | 3819 | 3278 | 5440 | 2770
2010 | 3545 | 2677 | 6108 | 2970
Wind Energy Modeling

## Slide 12
https://pvlib-python.readthedocs.io/en/latest/forecasts.htm
Time series of components of solar irradiance, GHI, DNI, DHI (W/m2)
Solar Energy Modeling

## Slide 13
https://pvlib-python.readthedocs.io/en/latest/forecasts.htm
Global Horizontal Irradiance (GHI) at the plane of array (POA)
Solar Energy Modeling

## Slide 14
Pvlib Toolbox from Sandia and NREL’s SAM package and Weather Data from GFS Global Model
system = {'module': module, 'inverter': inverter, ....: 'surface_azimuth': 180}
https://pvlib-python.readthedocs.io/en/latest/introexamples.html
# get the module and inverter specifications from SAM
sandia_modules = pvlib.pvsystem.retrieve_sam('SandiaMod')
module = sandia_modules['Canadian_Solar_CS5P_220M___2009_’]
Description: 220W Monocrystalline Module http://www.solarhub.com/solarhub_products/106-CS5P-220M-Canadian-Solar
sapm_inverters = pvlib.pvsystem.retrieve_sam('cecinverter’)
inverter = sapm_inverters['ABB__MICRO_0_25_I_OUTD_US_208_208V__CEC_2014_']
Considering other factors such as air temperature at the plane of array and the module efficiency .
Solar Energy Modeling
Convert GHI at the POA to Solar PV Power

## Slide 15
https://pvlib-python.readthedocs.io/en/latest/forecasts.htm
Time series of Solar Power (W)
Solar Energy Modeling

## Slide 16
2009 | Wh | NCF |  | 2010 | Wh | NCF
Charlotte | 446028 | 23.14% |  | Charlotte | 446035 | 23.14%
Boulder | 491571 | 25.51% |  | Boulder | 491582 | 25.51%
Boston | 451885 | 23.45% |  | Boston | 451899 | 23.45%
Tucson | 467719 | 24.27% |  | Tucson | 467726 | 24.27%
For 2009 and 2010, as in the wind energy modeling
Chart: Yearly Yield of Solar Energy
| Charlotte | Boulder | Boston | Tucson
2009 | 446.0278 | 491.5714 | 451.8849 | 467.7191
2010 | 446.0346 | 491.5816 | 451.8991 | 467.7258
Chart: Yearly Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
2009 | 0.23144 | 0.25507 | 0.23448 | 0.24269
2010 | 0.23144 | 0.25508 | 0.23448 | 0.2427
Solar Energy Modeling

## Slide 17
2009 | NCF | 
 | Wind Energy | Solar Energy
Charlotte | 29.10% | 23.14%
Boulder | 24.90% | 25.51%
Boston | 41.40% | 23.45%
Tucson | 21.10% | 24.27%
Chart: 2009 Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
Wind Energy | 0.291 | 0.249 | 0.414 | 0.211
Solar Energy | 0.23144 | 0.25507 | 0.23448 | 0.24269
Chart: 2010 Net Capacity Factor
| Charlotte | Boulder | Boston | Tucson
Wind Energy | 0.27 | 0.204 | 0.465 | 0.226
Solar Energy | 0.23144 | 0.25507 | 0.23448 | 0.24269
2010 | NCF | 
 | Wind Energy | Solar Energy
Charlotte | 27.00% | 23.14%
Boulder | 20.40% | 25.51%
Boston | 46.50% | 23.45%
Tucson | 22.60% | 24.27%
Comparison of NCF for Resources of Wind & Solar Energy
Wind and Solar Energy Modeling