## Slide 1
Hourly Probabilistic Solar Power Forecasts
Energy Production and Infrastructure Center
Department of Electrical and Computer Engineering
University of North Carolina at Charlotte
Mohamed Abuella
Prof. Badrul Chowdhury
September 18, 2017

## Slide 2
Hourly Probabilistic Forecasting of Solar Power
Overview of Solar Power Forecasting
Presentation Outline

## Slide 3
Renewables Generations
(Wind and Solar) are Too Variable
High Efficiency and Large Energy Storage
Still not Exist
Reducing
Cost
and Pollution
Why Forecast?
PG = PD + Ploss
Variable Generations (V.G.) Forecasting

## Slide 4
VG forecasting in US. electric utilities and ISO, such as CAISO, ERCOT, MISO, ISO-NE, NYISO,…etc.
Botterud, J. Wang, V. Miranda, and R. J. Bessa, “Wind power forecasting in US electricity markets,” The Electricity Journal, vol. 23, no. 3, pp. 71–82, 2010.
Elke Lorenz, “Solar Resource Forecasting” International Solar Energy Society (ISES) Webinar, 2016.
Voyant, C., Notton, G., Kalogirou, S., Nivet, M. L., Paoli, C., Motte, F., & Fouilloy, A. (2017). Machine learning methods for solar radiation forecasting: A review. Renewable Energy, 105, 569-582.
Forecast Horizons
Variable Generations (V.G.) Forecasting
Forecast horizons, forecasting models and the related applications of VG forecasts
Where Forecast?

## Slide 5
Flowchart of the Combined Approach (Physical and Statistical) of the Solar Power Forecasting
Regression
Extrapolation
Solar Power Forecasting
How Forecast?

## Slide 6: Flowchart of the Solar Power Forecasting
Hourly Probabilistic Forecasting of Solar Power

## Slide 7
Data Description:
PV solar system is near Canberra, Australia. The panel type is Solarfun SF160-24-1M195, consisting of 8 panels, its nominal power of (1560W), and panel orientation 38° clockwise from the north, with panel tilt (of 36°). The historical observed solar power data are normalized to the rated capacity (i.e., 1560W).
https://crowdanalytix.com/contests/global-energy-forecasting-competition-2014-probabilistic-solar-power-forecasting
http://www.ecmwf.int (European Centre for Medium-Range Weather Forecasts)
Training
Testing
Hourly Probabilistic Forecasting of Solar Power
The weather forecast data and the available measured solar power data from April 2012 to May 2014.
No. | Month | Year
1 | April | 2012
2 | May | 2012
3 | June | 2012
4 | July | 2012
5 | August | 2012
6 | September | 2012
7 | October | 2012
8 | November | 2012
9 | December | 2012
10 | January | 2013
11 | February | 2013
12 | March | 2013
13 | April | 2013
14 | May | 2013
15 | June | 2013
16 | July | 2013
17 | August | 2013
18 | September | 2013
19 | October | 2013
20 | November | 2013
21 | December | 2013
22 | January | 2014
23 | February | 2014
24 | March | 2014
25 | April | 2014
26 | May | 2014
Weather Variables | 
No. | Variable Name
1 | Cloud Water Content
2 | Cloud Ice Content
3 | Surface Pressure
4 | Relative Humidity
5 | Cloud Cover
6 | 10m-U Wind
7 | 10m-V Wind
8 | 2-m Temperature
9 | Surface solar radiation down
10 | Surface thermal radiation down
11 | Top net solar radiation
12 | Total precipitation
Weather predictions are produced by the global numerical weather prediction system (ECMWF).

## Slide 8
Multiple Linear Regression (MLR) Analysis, Artificial Neural Networks (ANN), and Support Vector Regression (SVR) are deployed for the short-term solar power forecasting.
Flowchart of the forecasting models
Training Set
Solar Power Forecast
Learning Algorithm
New Input X
Predicted Output Y
Flowchart of solar forecasting model building steps
Building the Model
Training
Validation
Testing
Forecasting Models
Parametric and Nonparametric Models
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.

## Slide 9
General diagram of combining different models
Model B
Model A
Model C
Model N
Method of Combining the Models
Combined Forecasts
Individual forecasting models
Combining Various Models
Methods of Combining The Models
Random forest (RF) is chosen to be the ensemble learning method for combining the various models’ outcomes.
Fcomb=WA*MA+ WB*MB + WC*MC ….+ WN*MN
WN is a weight is assigned to the outcome of a model MN
Ensemble Forecasts
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2nd Edition. Springer-Verlag New York, 2009.

## Slide 10
Day | Month
1 : | June
: | July
: : : | : : :
: | April
30 | May
31 | 00:00 : 23:00
Weather Data | 
: : | : :
: | :
: : : | : : :
: | :
: | :
: : : | : : :
PV Power | 
: : | (Past Observations)
: | 
: : : | 
: | 
: | 
Forecasts (Model’s Outcomes) | 
at 00:00
Day | Month
1 : | June
: | July
: : : | : : :
: | April
30 | May
31 | 00:00 : 23:00
Weather Data | 
: : | : :
: | :
: : : | : : :
: | :
: | :
: : : | : : :
Models’ Outcomes |  | 
: : | : : | : :
: | : | :
: : : | : : : | : : :
: | : | :
: | : | :
Forecasts |  | 
PV Power | 
: : | (Past Observations)
: | 
: : : | 
: | 
: | 
Combined Forecasts | 
(a)
(b)
Persistence model and day-ahead Forecasts from MLR, ANN and SVR
Combining by Radom Forest
Producing Different Models’ Outcomes
Schematic diagram of producing and ensemble different models’ outcomes
Ensemble Forecasts

## Slide 11
Each tree of the random forest is trained with random samples (random input dataset).
In the forecasting process (test) the trees give different forecasts, which can be then used for quantifying the uncertainty of the average output and producing the probabilistic forecasts.
The prediction of a given point x of the response variable is then obtained by averaging the individual trees outputs:
T. Hastie, R. Tibshirani, J. Friedman, and others, The elements of statistical learning, 2 Edition. Springer-Verlag New York, 2009.
Note: In fact, tree splitting is not simple as it seems,
since x can comes with dimensions up to 20 dimensions.
Probabilistic Forecasts
Ensemble-based probabilistic forecasts method:

## Slide 12
Analog Ensemble (AnEn) method:
S. Alessandrini, L. Delle Monache, S. Sperati, and G. Cervone, “An analog ensemble for short-term probabilistic solar power forecast,” Appl. Energy, vol. 157, pp. 95–110, 2015.
Probabilistic Forecasts
where denotes the given point forecast at an hour Hr, for which the prediction interval will be estimated, the point forecasts at the same hour of the day.
Notice that all values are normalized in the range [0, 1].
Schematic diagram of analog ensemble method
= 0.1

## Slide 13
Persistence probabilistic forecasts method:
Probabilistic Forecasts
Schematic diagram of analog ensemble method
The 10, 20 and 30 recent observed powers are carried out.
It is found that the recent 10 observed solar powers at the given hour with CDF distribution achieve more accurate persistence probabilistic forecasts.
No past forecasts are needed.

## Slide 14
Probabilistic Forecasts
Different distributions of probability
Probability distributions by the cumulative distribution function (CDF)
Linear CDF
Max
Min
to derive CDF
Parametric normal- distributed CDF
Mean
Std. dev.
to derive CDF.
Nonparametric CDF
No mean
neither Std. Dev.
CDF is estimated by piecewise nonparametric method
The probabilistic forecasts are estimated by using CDF-1
For example, for a given point forecast at 14:00, June 2nd 2013:
Histogram of the ensemble of RF’s outcomes

## Slide 15
The objective is to determine probabilistic solar forecasts in the form of probabilistic distribution (in quantiles) in incremental time steps through the forecast horizon.
A Pinball loss function is used to evaluate the accuracy of the probabilistic forecasts. It is a piecewise linear function which is often used to evaluate the accuracy of quantile forecasts.
J. M. Morales, A. J. Conejo, H. Madsen, P. Pinson, and M. Zugno, Integrating renewables in electricity markets - Operational problems, vol. 205. Boston, MA: Springer US, 2014.
where Pbq(F, P) is the pinball loss function to the probabilistic forecasts for each hour; is the forecasted value at the certain q quantile of the probabilistic solar power forecasts, and P is the observed value of the solar power. The quantile q has discrete values .For instance, q = 0.9 means that there is a 90% probability that the observed solar power will be less than the value of the 90th quantile.
Probabilistic Forecasts
Evaluation of probabilistic forecasts:

## Slide 16
Graphs of the probabilistic forecasts of the three methods for three days
Results and Evaluation
The lower Pinball (Pb) is, the more accurate probabilistic forecasts are.
Pinball loss function (Pb):

## Slide 17
Monthly Pinball of the probabilistic forecasts of the three methods
Results and Evaluation
Pinball loss function (Pb):
The lower Pinball (Pb) is, the more accurate probabilistic forecasts are.

## Slide 18
Results and Evaluation
Chart: The Improvements of Ensemble over Analog Ensemble
| June | July | August | September | October | November | December | January | February | March | April | May
AnEn | 0.016105 | -0.017583 | -0.050525 | 0.012754 | 0.0028841 | -0.016703 | 0.0071909 | 0.038367 | 0.058032 | -0.02011 | 0.034124 | 0.067554
Chart: Probabilistic Forecasts
| June | July | August | September | October | November | December | January | February | March | April | May
Persistence | 0.01658 | 0.017596 | 0.018245 | 0.017307 | 0.014922 | 0.019083 | 0.016202 | 0.017876 | 0.02146 | 0.020811 | 0.019437 | 0.013709
Analog Ensemble | 0.0096912 | 0.012198 | 0.011126 | 0.011633 | 0.009605 | 0.010398 | 0.0089507 | 0.0083014 | 0.01039 | 0.01281 | 0.010258 | 0.0085945
Ensemble | 0.0095352 | 0.012413 | 0.011689 | 0.011484 | 0.0095773 | 0.010571 | 0.0088863 | 0.0079829 | 0.0097872 | 0.013068 | 0.0099075 | 0.0080139

## Slide 19: Conclusions
The probabilistic forecasting are quantifying the uncertainty associated with point forecasts.
Combining the forecasts of various models leads to accurate point and probabilistic forecasts.
Throughout the complete year, the ensemble based-probabilistic forecasts are more accurate. than the analog ensemble and persistence probabilistic forecasts.
The random forest is a powerful ensemble learning method.
The CDF with the assumption of a normal distribution is better than the linear distribution to produce the probabilistic forecasts.
The nonparametric estimation of CDF without the normality assumption yields a small improvement (Pb=0.0100 vs. Pb=0.0102 with a normality assumption of CDF).
With additional historical data, the forecasting performance could be improved.

## Slide 20
Thanks for Your Listening
Any Question?
http://epic.uncc.edu/
Mohamed Abuella
mabuella@uncc.edu
Energy Production and Infrastructure Center
University of North Carolina at Charlotte